MODEL TOR FOR AN OPENCAST COALMINE PROJECT

- An EIA-EMP Report would be prepared for …….. MTPA rated capacity in an ML/project area of …… ha based on the generic structure specified in Appendix III of the EIA Notification 2006.

- An EIA-EMP Report would be prepared for ……. MTPA rated capacity cover the impacts and management plan for the project specific activities on the environment of the region, and the environmental quality – air, water, land, biotic community, etc. through collection of data and information, generation of data on impacts including prediction modelling for ………. MTPA of coal production based on approval of project/Mining Plan for ………MTPA. Baseline data collection can be for any season except monsoon.

- A map specifying locations of the State, District and Project location.

- A Study area map of the core zone and 10km area of the buffer zone (1: 50,000 scale) clearly delineating the major topographical features such as the land use, surface drainage of rivers/streams/nalas/canals, locations of human habitations, major constructions including railways, roads, pipelines, major industries/mines and other polluting sources. In case of ecologically sensitive areas such as Biosphere Reserves/National Parks/WL Sanctuaries/ Elephant Reserves, forests (Reserved/Protected), migratory corridors of fauna, and areas where endangered fauna and plants of medicinal and economic importance found in the 15 km area of the buffer zone should be given.

- Land use map (1: 50,000 scale) based on a recent satellite imagery of the study area may also be provided with explanatory note of the land use. Satellite imagery per se is not required.

- Map showing the core zone delineating the agricultural land (irrigated and unirrigated, uncultivable land (as defined in the revenue records), forest areas (as per records), along with other physical features such as water bodies, etc should be furnished.

- A contour map showing the area drainage of the core zone and 2-5 km of the buffer zone (where the water courses of the core zone ultimately join the major rivers/streams outside the lease/project area) should also be clearly indicated as a separate map.

- A detailed Site plan of the mine showing the various proposed break-up of the land for mining operations such as the quarry area, OB dumps, green belt, safety zone, buildings, infrastructure, CHP, ETP, Stockyard, township/colony (within and adjacent to the ML), undisturbed area and if any, in topography such as existing roads, drains/natural water bodies are to be left undisturbed along with any natural drainage adjoining the lease /project and modification of thereof in terms of construction of embankments/bunds, proposed diversion/rechannelling of the water courses, etc., approach roads, major haul roads, etc.

- In case of any proposed diversion of nallah/canal/river, the proposed route of diversion/modification of drainage and their realignment, construction of embankment etc. should also be shown on the map.

- Similarly if the project involves diversion of any road/railway line passing through the ML/project area, the proposed route of diversion and its realignment should be shown.

- Break up of lease/project area as per different land uses and their stage of acquisition.

LANDUSE DETAILS FOR OPENCAST PROJECT

| S.N. | LANDUSE | Within ML Area (ha) | Outside ML Area (ha) | TOTAL |
| --- | --- | --- | --- | --- |
| 1. | Agricultural land |  |  |  |
| 2. | Forest land |  |  |  |
| 3. | Wasteland |  |  |  |
| 4. | Grazing land |  |  |  |
| 5. | Surface water bodies |  |  |  |
| 6. | Settlements |  |  |  |
| 7. | Others (specify) |  |  |  |
|  | TOTAL |  |  |  |

- Break-up of lease/project area as per mining operations.

- Impact of changes in the land use due to the start of the projects if much of the land being acquired is agricultural land/forestland/grazing land.

- Collection of one-season (non-monsoon) primary baseline data on environmental quality - air (PM10, PM2.5, SOx, NOx and heavy metals such as Hg, Pb, Cr, As, etc), noise, water (surface and groundwater), soil along with one-season met data coinciding with the same season for AAQ collection period.

- Map of the study area (1: 50, 000 scale) (core and buffer zone clearly delineating the location of various stations superimposed with location of habitats, other industries/mines, polluting sources. The number and location of the stations in both core zone and buffer zone should be selected on the basis of size of lease/project area, the proposed impacts in the downwind (air)/downstream (surface water)/groundwater regime (based on flow). One station should be in the upwind/upstream/non-impact/non-polluting area as a control station. The monitoring should be as per CPCB guidelines and parameters for water testing for both ground water and surface water as per ISI standards and CPCB classification wherever applicable. Values should be provided based on desirable limits.

- Study on the existing flora and fauna in the study area (10km) carried out by an institution of relevant discipline and the list of flora and fauna duly authenticated separately for the core and buffer zone and a statement clearly specifying whether the study area forms a part of the migratory corridor of any endangered fauna. If the study area has endangered flora and fauna, or if the area is occasionally visited or used as a habitat by Schedule-I fauna, or if the project falls within 15 km of an ecologically sensitive area, or used as a migratory corridor then a comprehensive Conservation Plan should be prepared and submitted with EIA-EMP Report and comments from the CWLW of the State Govt. also obtained and furnished.

- Details of mineral reserves, geological status of the study are and the seams to be worked, ultimate working depth and progressive stage-wise working scheme until end of mine life should be reflected on the basis of the approved rated capacity and calendar plans of production from the approved Mining Plan. Geological maps and sections should be included. The progressive mine development and Conceptual Final Mine Closure Plan should also be shown in figures.

- Details of mining methods, technology, equipment to be used, etc., rationale for selection of that technology and equipment proposed to be used vis-à-vis the potential impacts.

- Impact of mining on hydrology, modification of natural drainage, diversion and channelling of the existing rivers/water courses flowing though the ML and adjoining the lease/project and the impact on the existing users and impacts of mining operations thereon.

- Detailed water balance should be provided. The break up of water requirement for the various mine operations should be given separately.

- Source of water for use in mine, sanction of the competent authority in the State Govt. and impacts vis-à-vis the competing users.

- Impact of mining and water abstraction use in mine on the hydrogeology and groundwater regime within the core zone and 10 km buffer zone including long–term modelling studies on. Details of rainwater harvesting and measures for recharge of groundwater should be reflected in case there us a declining trend of groundwater availability and/or if the area falls within dark/grey zone.

- Impact of blasting, noise and vibrations.

- Impacts of mining on the AAQ, predictive modelling using the ISCST-3 (Revised) or latest model.

- Impacts of mineral transportation – within and outside the lease/project along with flow-chart indicating the specific areas generating fugitive emissions. Impacts of transportation, handling, transfer of mineral and waste on air quality, generation of effluents from workshop, management plan for maintenance of HEMM, machinery, equipment. Details of various facilities to be provided in terms of parking, rest areas, canteen, and effluents/pollution load from these activities.

- Details of waste generation – OB, topsoil – as per the approved calendar programme, and their management shown in figures as well explanatory chapter with tables giving progressive development and mine closure plan, green belt development, backfilling programme and conceptual post mining land use. OB dump heights and terracing should based on slope stability studies with a max of 28o angle as the ultimate slope. Sections of dumps (ultimate) (both longitudinal and cross section) with relation to the adjacent area should be shown.

| Project | Total waste generation (Mm3) | Topsoil (Mm3) | Total OB generation (Mm3) | Total OB in Ext. Dump | Total OB Backfilled (Mm3) |
| --- | --- | --- | --- | --- | --- |
| Original Project (ha) |  |  |  |  |  |
| Expansion Project (ha) (balance life) |  |  |  |  |  |
| TOTAL (Mm3) |  |  |  |  |  |

- Progressive Green belt and afforestation plan (both in text, figures as well as in tables prepared by MOEF) and selection of species (local) for the afforestation/plantation programme based on original survey/landuse.

Table 1: Stage-wise Landuse and Reclamation Area (ha)

| S.N. | Land use Category | Present (1st Year) | 5th Year | 10th Year | 20th year | 24th Year (end of Mine life)* |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Backfilled Area (Reclaimed with plantation) |  |  |  |  |  |
| 2. | Excavated Area (not reclaimed)/void |  |  |  |  |  |
| 3. | External OB dump Reclaimed with plantation) |  |  |  |  |  |
| 4. | Reclaimed Top soil dump |  |  |  |  |  |
| 5. | Green Built Area |  |  |  |  |  |
| 6. | Undisturbed area (brought under plantation) |  |  |  |  |  |
| 7. | Roads (avenue plantation) |  |  |  |  |  |
| 8. | Area around buildings and Infrastructure |  |  |  |  |  |
|  | TOTAL | 110* | 110* | 110* | 110* | 110* |

* As a representative example

Table 2: Stage-wise Cumulative Plantation

| S.N. | YEAR* | Green Belt | External Dump | Backfilled Area | Others (Undisturbed Area/etc) | TOTAL |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Area (ha) | No. of trees | Area (ha) | No. of Trees | Area (ha) | No. of Trees | Area (ha) | No. of Trees | Area (ha) | No. of Trees |
| 1. | 1st year |  |  |  |  |  |  |  |  |  |  |
| 2. | 3rd year |  |  |  |  |  |  |  |  |  |  |
| 3. | 5th year |  |  |  |  |  |  |  |  |  |  |
| 4. | 10th yesr |  |  |  |  |  |  |  |  |  |  |
| 5. | 15th year |  |  |  |  |  |  |  |  |  |  |
| 6. | 20th year |  |  |  |  |  |  |  |  |  |  |
| 7. | 25th year |  |  |  |  |  |  |  |  |  |  |
| 8. | 30th year |  |  |  |  |  |  |  |  |  |  |
| 9. | 34th year (end of mine life) |  |  |  |  |  |  |  |  |  |  |
| 10. | 34-37th Year (Post-mining) |  |  |  |  |  |  |  |  | 85 |  |

* As a representative example

- Conceptual Final Mine Closure Plan, post mining land use and restoration of land/habitat to pre- mining. A Plan for the ecological restoration of the area post mining and for land use should be prepared with detailed cost provisions. Impact and management of wastes and issues of rehandling (wherever applicable) and backfilling and progressive mine closure and reclamation.

Table 3: Post-Mining Landuse Pattern of ML/Project Area (ha)

| S.N. | Land use during Mining | Land Use (ha) |
| --- | --- | --- |
| 1. | External OB Dump | Plantation | Water Body | Public Use | Undisturbed | TOTAL |
| 2. | Top soil Dump |  |  |  |  |  |
| 3. | Excavation |  |  |  |  |  |
| 4. | Roads |  |  |  |  |  |
| 4. | Built up area |  |  |  |  |  |
| 5. | Green Belt |  |  |  |  |  |
| 6. | Undisturbed Area |  |  |  |  |  |
|  | TOTAL | 85 |  |  |  | 110 |

- Flow chart of water balance. Treatment of effluents from workshop, township, domestic wastewater, mine water discharge, etc. Details of STP in colony and ETP in mine. Recycling of water to the max. possible extent.

- Occupational health issues. Baseline data on the health of the population in the impact zone and measures for occupational health and safety of the personnel and manpower for the mine.

- Risk Assessment and Disaster Preparedness and Management Plan.

- Integrating in the Env. Management Plan with measures for minimising use of natural resources - water, land, energy, etc.

- Including cost of EMP (capital and recurring) in the project cost and for progressive and final mine closure plan.

- Details of R&R.  Detailed project specific R&R Plan with data on the existing socio-economic status of the population (including tribals, SC/ST, BPL families) found in the study area and broad plan for resettlement of the displaced population, site for the resettlement colony, alternate livelihood concerns/employment for the displaced people, civic and housing amenities being offered, etc and costs along with the schedule of the implementation of the R&R Plan.

- CSR Plan along with details of villages and specific budgetary provisions (capital and recurring) for specific activities over the life of the project.

- Public Hearing should cover the details of notices issued in the newspaper, proceedings/minutes of public hearing, the points raised by the general public and commitments made by the proponent should be presented in a tabular form. If the Public Hearing is in the regional language, an authenticated English Translation of the same should be provided.

- In built mechanism of self-monitoring of compliance of environmental regulations.

(xxxx)  Status of any litigations/ court cases filed/pending on the project.

(xxxxi) Submission of sample test analysis of:

Characteristics of coal - this includes grade of coal and other characteristics – ash, S and heavy metals including levels of Hg, As, Pb, Cr etc.

(xxxxii) Copy of clearances/approvals – such as Forestry clearances, Mining Plan Approval,

NOC from Flood and Irrigation Dept. (if req.), etc. wherever applicable.

(A) FORESTRY CLEARANCE

| TOTAL ML/PROJECT AREA (ha) | TOTAL FORESTLAND (ha) | Date of FC | Extent of forestland | Balance area for which FC is yet to be obtained | Status of appl. for diversion of forestland |
| --- | --- | --- | --- | --- | --- |
|  |  | If more than one, provide details of each FC |  |  |  |

(B)	MINING PLAN/PROJECT APPROVAL

Date of Approval of Mining Plan/Project Approval:

Copy of Letter of Approval of Mining Plan/Project Approval

(xxxviii) Corporate Environment Responsibility:

a) 	The Company must have a well laid down Environment Policy approved by the Board of Directors.

b)	The Environment Policy must prescribe for standard operating process/procedures to bring into focus any infringements/deviation/violation of the environmental or forest norms/conditions.

c)  	The hierarchical system or Administrative Order of the company to deal with environmental issues and for ensuring compliance with the environmental clearance conditions must be furnished.

d)  To have proper checks and balances, the company should have a well laid down system of reporting of non-compliances/violations of environmental norms to the Board of Directors of the company and/or shareholders or stakeholders at large.

GENERAL CONDITIONS AND ADDITIONAL POINTS OF TOR

The following general points should be noted:

(i)	All documents should be properly indexed, page numbered.

(ii)	Period/date of data collection should be clearly indicated.

(iii)	Authenticated English translation of all material provided in Regional languages.

(iv)	After the preparation of the draft EIA-EMP Report as per the aforesaid TOR, the proponent shall get the Public Hearing conducted as prescribed in the EIA Notification 2006 and take necessary action for obtaining environmental clearance under the provisions of the EIA Notification 2006.

- The letter/application for EC should quote the MOEF file No. and also attach a copy of the letter prescribing the TOR.

- The copy of the letter received from the Ministry on the TOR prescribed for the project should be attached as an annexure to the final EIA-EMP Report.

(vii)	The final EIA-EMP report submitted to the Ministry must incorporate the issues in TOR and that raised in Public Hearing. The index of the final EIA-EMP report, must indicate the specific chapter and page no. of the EIA-EMP Report where the specific TOR prescribed by Ministry and the issue raised in the P.H. have been incorporated. Mining Questionnaire (posted on MOEF website) with all sections duly filled in shall also be submitted at the time of applying for EC.

(viii)	General Instructions for the preparation and presentation before the EAC of TOR/EC projects of Coal Sector should be incorporated/followed.

(viii)	The aforesaid TOR has a validity of two years only.

The following additional points are also to be noted:

- Grant of TOR does not necessarily mean grant of EC.

- Grant of TOR/EC to the present project does not necessarily mean grant of TOR/EC to the captive/linked project.

- Grant of TOR/EC to the present project does not necessarily mean grant of approvals in other regulations such as the Forest (Conservation) Act 1980 or the Wildlife (Protection) Act, 1972.

(iv)	Grant of EC is also subject to Circulars issued under the EIA Notification 2006, which are available on the MOEF website: www.envfor.nic.in

______

MODEL TOR FOR AN UNDERGROUND COALMINE PROJECT

- An EIA-EMP Report should be prepared for a peak capacity of  ………….. MTPA over an area of  ………….. ha  addressing the impacts of the underground coalmine project including the aspects of mineral transportation and issues of impacts on hydrogeology, plan for conservation of flora/fauna and afforestation/plantation programme based on the generic structure specified in Appendix III of the EIA Notification 2006.. Baseline data collection can be for any season except monsoon.

- The EIA-EMP report should also cover the impacts and management plan for the project specific activities on the environment of the region, and the environmental quality – air, water, land, biotic community, etc. through collection of baseline data and information, generation of baseline data on impacts for ……. MTPA of coal production based on approval of project/Mining Plan.

- A Study area map of the core zone and 10km area of the buffer zone (15 km of the buffer zone in case of ecologically sensitive areas) delineating the major topographical features such as the land use, drainage, locations of habitats, major construction including railways, roads, pipelines, major industries/mines and other polluting sources, which shall also indicate the migratory corridors of fauna, if any and the areas where endangered fauna and plants of medicinal and economic importance are found in the area.

- Map showing the core zone along with 3-5 km of the buffer zone) delineating the agricultural land (irrigated and unirrigated, uncultivable land (as defined in the revenue records), forest areas (as per records) and grazing land and wasteland and water bodies.

- Contour map at 3m interval along with Site plan of the mine (lease/project area with about 3-5 km of the buffer zone) showing the various surface structures such as buildings, infrastructure, CHP, ETP, Stockyard, township/colony (within/adjacent to the ML), green belt and undisturbed area and if any existing roads, drains/natural water bodies are to be left undisturbed along with details of natural drainage adjoining the lease/project and modification of thereof in terms of construction of embankments/bunds, proposed diversion/rechannelling of the water courses, etc., highways, passing through the lease/project area.

- Original land use (agricultural land/forestland/grazing land/wasteland/water bodies) of the area. Impacts of project, if any on the landuse, in particular, agricultural land/forestland/grazing land/water bodies falling within the lease/project and acquired for mining operations. Extent of area under surface rights and under mining rights.

| S.N. | ML/Project Land use | Area under Surface Rights (ha) | Area Under Mining Rights (ha) | Area under Both (ha) |
| --- | --- | --- | --- | --- |
| 1. | Agricultural land |  |  |  |
| 2. | Forest Land |  |  |  |
| 3. | Grazing Land |  |  |  |
| 4. | Settlements |  |  |  |
| 5. | Others (specify) |  |  |  |

Area Under Surface Rights

| S.N. | Details | Area (ha) | Forestland (ha) | Agr. land (ha) | Wasteland (ha) | Settlements (ha) | Others (ha) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Buildings |  |  |  |  |  |  |
| 2. | Infrastructure |  |  |  |  |  |  |
| 3. | Roads |  |  |  |  |  |  |
| 4. | Others (specify) |  |  |  |  |  |  |
|  | TOTAL |  |  |  |  |  |  |

- Study on the existing flora and fauna in the study area carried out by an institution of relevant discipline and the list of flora and fauna duly authenticated separately for the core and buffer zone and a statement clearly specifying whether the study area forms a part of the migratory corridor of any endangered fauna. The flora and fauna details should be furnished separately for the core zone and buffer zone. The report and the list should be authenticated by the concerned institution carrying out the study and the names of the species scientific and common names) along with the classification under the Wild Life Protection Act, 1972 should be furnished.

- Details of mineral reserves, geological status of the study area and the seams to be worked, ultimate working depth and progressive stage-wise working plan/scheme until end of mine life should be reflected on the basis of the approved rated capacity and calendar plans of production from the approved Mining Plan. Geological maps should also be included.

- Impact of mining on hydrology, modification of natural drainage, diversion and channelling of the existing rivers/water courses flowing though the ML and adjoining the lease/project and the impact on the existing users and impacts of mining operations thereon.

- Collection of one-season (non-monsoon) primary baseline data on environmental quality – air (PM10, PM2.5, SOx, NOx and heavy metals such as Hg, Pb, Cr, AS, etc), noise, water (surface and groundwater), soil along with one-season met data.

- Map of the study area (core and buffer zone) clearly delineating the location of various monitoring stations (air/water/soil and noise – each shown separately) superimposed with location of habitats, wind roses, other industries/mines, polluting sources. The number and location of the stations should be selected on the basis of the proposed impacts in the downwind/downstream/groundwater regime. One station should be in the upwind/upstream/non-impact non-polluting area as a control station. Wind roses to determine air pollutant dispersion and impacts thereof shall be determined. Monitoring should be as per CPCB guidelines and standards for air, water, noise notified under Environment Protection Rules. Parameters for water testing for both ground and surface water should be as per ISI standards and CPCB classification of surface water wherever applicable.

- Impact of mining and water abstraction and mine water discharge in mine on the hydrogeology and groundwater regime within the core zone and 10km buffer zone including long–term modelling studies on the impact of mining on the groundwater regime. Details of rainwater harvesting and measures for recharge of groundwater should be reflected wherever the areas are declared dark/grey from groundwater development.

- Study on subsidence, measures for mitigation/prevention of subsidence, modelling subsidence prediction and its use during mine operation, safety issues.

- Detailed water balance should be provided. The break up of water requirement as per different activities in the mining operations, including use of water for sand stowing should be given separately. Source of water for use in mine, sanction of the competent authority in the State Govt. and impacts vis-à-vis the competing users should be provided.

- Impact of choice of mining method, technology, selected use of machinery - and impact on air quality, mineral transportation, coal handling & storage/stockyard, etc, Impact of blasting, noise and vibrations.

- Impacts of mineral transportation – within and outside the lease/project. The entire sequence of mineral production, transportation, handling, transfer and storage of mineral and waste, and their impacts on air quality should be shown in a flow chart with the specific points where fugitive emissions can arise and the specific pollution control/mitigative measures proposed to be put in place. Examine the adequacy of roads existing in the area and if new roads are proposed, the impact of their construction and use particularly if forestland is used.

- Details of various facilities to be provided in terms of parking, rest areas, canteen, and effluents/pollution load from these activities.  Examine whether existing roads are adequate to take care of the additional load of mineral and their impacts.

- Examine the number and efficiency of mobile/static water sprinkling system along the main mineral transportation road within the mine, approach roads to the mine/stockyard/siding, and also the frequency of their use in impacting air quality.

- Impacts of CHP, if any on air and water quality. A flow chart of water use and whether the unit can be made a zero-discharge unit.

- Conceptual Final Mine Closure Plan along with the fund requirement for the detailed activities proposed there under.  Impacts of change in land use for mining operations and whether the land can be restored for agricultural use post mining.

Table 1 Stage-wise Cumulative Plantation

| S.N. | YEAR* | Green Belt | External Dump | Backfilled Area | Others (Undisturbed Area/etc) | TOTAL |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Area (ha) | No. of trees | Area (ha) | No. of Trees | Area (ha) | No. of Trees | Area (ha) | No. of Trees | Area (ha) | No. of Trees |
| 1. | 1st year |  |  |  |  |  |  |  |  |  |  |
| 2. | 3rd year |  |  |  |  |  |  |  |  |  |  |
| 3. | 5th year |  |  |  |  |  |  |  |  |  |  |
| 4. | 10th yesr |  |  |  |  |  |  |  |  |  |  |
| 5. | 15th year |  |  |  |  |  |  |  |  |  |  |
| 6. | 20th year |  |  |  |  |  |  |  |  |  |  |
| 7. | 25th year |  |  |  |  |  |  |  |  |  |  |
| 8. | 30th year |  |  |  |  |  |  |  |  |  |  |
| 9. | 34th year (end of mine life) |  |  |  |  |  |  |  |  |  |  |
| 10. | 34-37th Year (Post-mining) |  |  |  |  |  |  |  |  | 85* | 2,12,500 |

*As a representative example

- Occupational health issues. Baseline data on the health of the population in the impact zone and measures for occupational health and safety of the personnel and manpower for the mine should be furnished.

- Details of cost of EMP (capital and recurring) in the project cost and for final mine closure plan. The specific costs (capital and recurring) of each pollution control/mitigative measures proposed in the project until end of mine life and a statement that this is included in the project cost.

- Integrating in the Env. Management Plan with measures for minimising use of natural resources – water, land, energy, raw materials/mineral, etc.

- R&R: Detailed project specific R&R Plan with data on the existing socio-economic status (including tribals, SC/ST) of the population in the study area and broad plan for resettlement of the displaced population, site for the resettlement colony, alternate livelihood concerns/employment for the displaced people, civic and housing amenities being offered, etc and costs along with the schedule of the implementation of the R&R Plan.

- CSR Plan along with details of villages and specific budgetary provisions (capital and recurring) for specific activities over the life of the project.

- Public Hearing should cover the details as specified in the EIA Notification 2006, and include notices issued in the newspaper, proceedings/minutes of public hearing, the points raised by the general public and commitments by the proponent made should be presented in a tabular form. If the Public Hearing is in the regional language, an authenticated English Translation of the same should be provided.

- Status of any litigations/ court cases filed/pending in any Court/Tribunal on the project should be furnished.

- Submission of sample test analysis of:

(xxxvii) Characteristics of coal - this includes grade of coal and other characteristics – ash, S

and heavy metals including levels of Hg, As, Pb, Cr etc.

(xxxviii) Copy of clearances/approvals – such as Forestry clearances, Mining Plan Approval, NOC from Flood and Irrigation Dept. (if req.), etc.

(A) FORESTRY CLEARANCE

| TOTAL ML/PROJECT AREA (ha) | TOTAL FORESTLAND (ha) | Date of FC | Extent of forestland | Balance area for which FC is yet to be obtained | Status of appl. for diversion of forestland |
| --- | --- | --- | --- | --- | --- |
|  |  | If more than one, provide details of each FC |  |  |  |

(B)	MINING PLAN /PROJECT APPROVAL

Date of Approval of Mining Plan/Project Approval:

Copy of Letter of Approval of Mining Plan/Project Approval

(xxxviii) Corporate Environment Responsibility:

a) 	The Company must have a well laid down Environment Policy approved by the Board of Directors.

b)	The Environment Policy must prescribe for standard operating process/procedures to bring into focus any infringements/deviation/violation of the environmental or forest norms/conditions.

c)  	The hierarchical system or Administrative Order of the company to deal with environmental issues and for ensuring compliance with the environmental clearance conditions must be furnished.

d)  To have proper checks and balances, the company should have a well laid down system of reporting of non-compliances/violations of environmental norms to the Board of Directors of the company and/or shareholders or stakeholders at large.

GENERAL CONDITIONS AND ADDITIONAL POINTS OF TOR

The following general points should be noted:

(i)	All documents should be properly indexed, page numbered.

(ii)	Period/date of data collection should be clearly indicated.

(iii)	Authenticated English translation of all material provided in Regional languages.

(iv)	After the preparation of the draft EIA-EMP Report as per the aforesaid TOR, the proponent shall get the Public Hearing conducted as prescribed in the EIA Notification 2006 and take necessary action for obtaining environmental clearance under the provisions of the EIA Notification 2006.

- The letter/application for EC should quote the MOEF file No. and also attach a copy of the letter prescribing the TOR.

- The copy of the letter received from the Ministry on the TOR prescribed for the project should be attached as an annexure to the final EIA-EMP Report.

(vii)	The final EIA-EMP report submitted to the Ministry must incorporate the issues in TOR and that raised in Public Hearing. The index of the final EIA-EMP report, must indicate the specific chapter and page no. of the EIA-EMP Report where the specific TOR prescribed by Ministry and the issue raised in the P.H. have been incorporated. Mining Questionnaire (posted on MOEF website) with all sections duly filled in shall also be submitted at the time of applying for EC.

(viii)	General Instructions for the preparation and presentation before the EAC of TOR/EC projects of Coal Sector should be incorporated/followed.

(viii)	The aforesaid TOR has a validity of two years only.

The following additional points are also to be noted:

- Grant of TOR does not necessarily mean grant of EC.

- Grant of TOR/EC to the present project does not necessarily mean grant of TOR/EC to the captive/linked project and vice-versa.

- Grant of TOR/EC to the present project does not necessarily mean grant of approvals in other regulations such as the Forest (Conservation) Act 1980 or the Wildlife (Protection) Act, 1972 and vice versa.

(iv)	Grant of EC is also subject to Circulars issued under the EIA Notification 2006, which are available on the MOEF website: www.envfor.nic.in

______

Updated/ December, 2014

Generic ToR for coal washery

- Siting of washery is critical considering to its environmental impacts. Preference should be given to the site located at pit head; in case such a site is not available, the site should be as close to the pit head as possible and coal should be transported from mine to the washery preferably through closed conveyer belt to avoid air pollution.

- The washery shall not be located in eco-sensitive zones areas.

- The washery should have a closed system and zero discharge. The storm drainage should be treated in settling ponds before discharging into rivers/streams/water bodies.

- A thick Green belt of about 50 m width should be developed surrounding the washery.

- A brief description of the plant alongwith a layout, the specific technology used and the source of coal should be provided.

- The EIA-EMP Repot should cover the impacts and management plan for the project of the capacity for which EC is sought and the impacts of specific activities, including the technology used and coal used, on the environment of the area (within 10km radius), and the environmental quality of air, water, land, biotic community, etc. through collection of data and information, generation of data on impacts for the rated capacity. Cumulative impacts for air and water should be a part of ElA in case coal mine, TPP and other washeries are located within 10km radius. The ElA should also include mitigative measures needed to minimize adverse environmental impacts.

- A Study Area Map of the core zone as well as the 10km area of buffer zone showing major industries/mines and other polluting sources should be submitted.These maps shall also indicate the migratory corridors of fauna, if any and areas of endangered fauna; plants of medicinal and economic importance; any ecologically sensitive areas within the 10 km buffer zone; the shortest distance from the National Park/WL Sanctuary Tiger Reserve, etc. alongwith the comments of the Chief Wildlife Warden of the State Government.

- Data of one-season (non-monsoon) primary- base-line data on environmental quality of air (PM10, PM2.5, SOx and NOx, noise, water (surface and groundwater), soil be submitted.

- The wet washery should generally utilize mine water only. In case mine water is not available, the option of storage of rain water and its use should be examined. Use of surface water and ground water should be avoided.

- Detailed water balance should be provided. The break-up of water requirement as per different activities in the mining operations vis-a-vis washery should be given. If the source of water is from surface water and/or ground water, the same may be justified besides obtaining approval of the Competent Authority for its drawl.

- The entire sequence of mineral production, transportation, handling, transfer and storage of mineral and waste, if any, and their impacts on air quality should be shown in a flow chart with specific points where fugitive emissions can arise and specific pollution control/mitigative measures proposed to be put in place. The washed coal and rejects should be transport by train as far as possible. Road transport of washed coal and rejects should generally be avoided. In case, the TPP is within 10km radius, it should be through conveyer belt. If transport by rail is not feasible because of the topography of the area, the option for transport by road be examined in detail and its impacts along with the mitigation measures should be clearly brought out in ElA/EMP report.

- Details of various facilities proposed to be provided in terms of parking, rest areas, canteen etc.to the personnel involved in mineral transportation, workshop and effluents/pollution load from these activities should be provided.

- Impacts of CHP, if any, on air and water quality should also be spelt out alongwith Action Plan.

- O.M. no. J-llOI3/25/2014-IA.I dated 11thAugust, 2014 to be followed with regard to CSR activities.

- Details of Public Hearing, Notice(s) issued in newspapers,proceedings/minutes of Public Hearing, points raised by the general public and response/commitments made by the proponent along with the Action Plan and budgetary provisions be submitted in tabular form. If the Public Hearing is in the regional language, an authenticated English translation of the same should be provided. Status of any litigations/ court cases filed/pending, if any, against the project should be mentioned in EIA.

- Analysis of samples indicating the following be submitted:

a. Characteristics of coal prior to washing (this includes grade of coal, other characteristics of ash, S and heavy levels of metals such as Hg, As, Pb, Cr etc).

b. Characteristics and quantum of coal after washing.

c. Characteristics and quantum of coal rejects.

- Details of management/disposal/use of coal rejects should be provided. The rejects should be used in TPP located close to the washery as far as possible. If TPP is within a reasonable distance (10 km), transportation should be by conveyor belt. If it is far away, the transportation should be by rail as far as possible.

- Copies of MOU/Agreement with linkages (for stand-alone washery) for the capacity for which EC is being sought should be submitted.

- Corporate Environment Responsibility:

a. The Company must have a well laid down Environment Policy approved by the Board of Directors.

b. The Environment Policy must prescribe for standard operating process/procedures to bring into focus any infringements/deviation/violation of the environmental or forest norms/conditions.

c. The hierarchical system or Administrative Order of the company to deal with environmental issues and for ensuring compliance with the environmental clearance conditions must be furnished.

d. To have proper checks and balances, the company should have a well laid down system of reporting of non-compliances/violations of environmental norms to the Board of Directors of the company and/or shareholders or stakeholders at large.

- A detailed action Plan for Corporate Social Responsibility for the project affected people and people living in and around the project area should be provided.

- Permission of drawl of water shall be pre-requisite for consideration of EC.

- Wastewater /effluent should confirm to the effluent standards as prescribed under Environment (Protection) Act, 1986

- Details of washed coal, middling and rejects along with the MoU with the end-users should be submitted.

*****

GENERAL CONDITIONS AND ADDITIONAL POINTS OF TOR

The following general points should be noted:

(i)	All documents should be properly indexed, page numbered.

(ii)	Period/date of data collection should be clearly indicated.

(iii)	Authenticated English translation of all material provided in Regional languages.

(iv)	After the preparation of the draft EIA-EMP Report as per the aforesaid TOR, the proponent shall get the Public Hearing conducted as prescribed in the EIA Notification 2006 and take necessary action for obtaining environmental clearance under the provisions of the EIA Notification 2006.

- The letter/application for EC should quote the MOEF file No. and also attach a copy of the letter prescribing the TOR.

- The copy of the letter received from the Ministry on the TOR prescribed for the project should be attached as an annexure to the final EIA-EMP Report.

(vii)	The final EIA-EMP report submitted to the Ministry must incorporate the issues in TOR and that raised in Public Hearing. The index of the final EIA-EMP report, must indicate the specific chapter and page no. of the EIA-EMP Report where the specific TOR prescribed by Ministry and the issue raised in the P.H. have been incorporated. Mining Questionnaire (posted on MOEF website) with all sections duly filled in shall also be submitted at the time of applying for EC.

(viii)	General Instructions for the preparation and presentation before the EAC of TOR/EC projects of Coal Sector should be incorporated/followed.

(viii)	The aforesaid TOR has a validity of two years only.

The following additional points are also to be noted:

- Grant of TOR does not necessarily mean grant of EC.

- Grant of TOR/EC to the present project does not necessarily mean grant of TOR/EC to the captive/linked project and vice-versa.

- Grant of TOR/EC to the present project does not necessarily mean grant of approvals in other regulations such as the Forest (Conservation) Act 1980 or the Wildlife (Protection) Act, 1972 and vice-versa.

(iv)	Grant of EC is also subject to Circulars issued under the EIA Notification 2006, which are available on the MOEF website: www.envfor.nic.in

______